Yaffs Tuning

Charles Manning
2013-05-15

Yaffs has many options for tuning for speed or memory use. This document details them for Yaffs Direct and Linux, covering compile time flags and settings, initialisation parameters, tracing, and state inspection.

# Yaffs Direct Configuration
Yaffs behaviour is dictated by compile time and run-time flags and parameters. This document outlines the most important ones.

There are many other options not discussed here which may be tweaked with some extra knowledge. It is best to contact Charles Manning or someone else closely associated with Yaffs to tweak thses settings.
## Compile Time Configurations
These setting are used to apply compile-time configurations. They are all of the form CONFIG_YAFFS_xxx

CONFIG_YAFFS_ALWAYS_CHECK_CHUNK_ERASED
Normally Yaffs checks that chunks are erased only on the first chunk write to each block. This flag allows you to force all chunks to be checked. This is slower, but is worth using when doing early debugging.
CONFIG_YAFFS_CASE_INSENSITIVE
When selected case insensitive name comparisons are used. Note that this will not magically change Yaffs to be case insensitive in a case sensitive OS. This needs to be set according to the OS policy. Typically this is only used in Windows CE.
CONFIG_YAFFS_DIRECT
Used when compiling Yaffs Direct.
CONFIG_YAFFS_DISABLE_LAZY_LOAD
Lazy loading is used to defer loading up object details until the objects are accessed. This makes mount time faster. This flag can disable lazy loading. Debug only.
CONFIG_YAFFS_ECC_WRONG_ORDER
This flag should only be used with old Linux MTD code which had a bug in the ECC byte ordering.
CONFIG_YAFFS_NO_YAFFS1
Used to say that only Yaffs2 operation should be compiled in. Not currently supported.
CONFIG_YAFFS_SHORT_NAMES_IN_RAM
Set to configure Yaffs to store short object names in RAM. This is faster, but uses up more memory.
CONFIG_YAFFS_UNICODE
Set to configure Yaffs to use Unicode file names (eg. With WinCE).
CONFIG_YAFFS_AUTO_UNICODE
Set to configure Yaffs to automatically use ASCII names when it can and Unicode names when it can't. Only useful when CONFIG_YAFFS_UNICODE is enabled..
CONFIG_YAFFS_UTIL
Used when compiling Yaffs for utilities.
CONFIG_YAFFS_WINCE
Set when compiling Yaffs for WinCE.
CONFIG_YAFFS_YAFFS2
Set when using Yaffs2 mode. At present this must always be set.
CONFIG_YAFFS_DEFINES_TYPES
CONFIG_YAFFSFS_PROVIDE_VALUES
Used when compiling Yaffs Direct only.

## Initialisation Parameters
Each yaffs device is configured by a yaffs_param structure which is part of the yaffs_dev structure. This contains the following fields:
name	A name for the device. In Yaffs Direct this is used as the mountpoint name for the device.
inband_tags	Yaffs2 only:If non-zero then use inband tags with tags being stored in the data area.. If zero, palce tags in spare area. If inbandTags is set then the short op cache must be enabled (ie n_caches must be non-zero.)
total_bytes_per_chunk	The number of bytes in the data area of the flash page. If inband_tags is not set then this whole area will be used to store data and the tags will be stored in the spare area. If inband_tags is set then part of this area will be used to store tags and the rest will be used to store data.
chunks_per_block	Number of chunks in a block.
spare_bytes_per_chunk	The number of available bytes in the spare area of the flash page. This excludes space used by ECC, bad block markers etc.
start_block	The first block in the partition to be used. 0 for first block.
end_block	The last block in the partition to be used.

n_reserved_blocks	Number of good blocks blocks reserved for garbage collection etc. Needs to be at least 2, but 5 would be a more typical number.
n_caches	Number of chunks to store in the short operation cache. Zero disables caching. Typical value is 10 to 20 or so. Caching is required for inband tags.
cache_bypass_aligned	If non-zero then aligned writes will bypass the cache (only used when inband tags is not enabled).
use_nand_ecc	Yaffs1 only: Flag indicating whether the driver performs ECC. If this is zero then Yaffs will perform ECC using SmartMedia-type ECC placement..
tags_9bytes	Use 9-byte tags
no_tags_ecc	Yaffs2 only: Flag indicating that the tags do not have any ECC stored with them.
is_yaffs2	Flag indicating if this is using the Yaffs2 mechanism. If this is not set then Yaffs1 mode of operation is provided.

empty_lost_n_found	Flag to delete all files in lost and found on mount.
skip_checkpt_rd	Yaffs2 only: Flag to skip reading checkpoint on mount. If set then a re-scan is forced.
skip_checkpt_wr	Yaffs2 only: Flag to skip writing checkpoint on sync or unmount.
refresh_period	Yaffs2 only: How often Yaffs should do a block refresh. Values less than 10 disable block refreshing. Typical values would be1000.
enable_xattr	Flag to enable the use of extended attributes (xattr).
max_objects	Limit the maxumum number of objects in a file system. 0 = no limit.

use_header_file_size	Debug only.
disable_lazy_loading	Debug only.
wide_tnodes_disabled	Debug only.
disable_soft_del	Yaffs1 only: Flag to disable soft deletion.
defered_dir_update	Set to defer directory updates.
auto_unicode	Enable automatic ASCII/Unicode handling. Only works when operating with Unicode enabled.
disable_summary	Disable reading/writing block summary info.

## Driver functions
The driver functions are stored in a yaffs_driver structure which is part of a yaffs_dev structure. These functions must be defined before the yaffs_dev is mounted.
drv_write_chunk_fn	Function to write a chunk
drv_read_chunk_fn	Function to read a chunk
drv_erase_fn	Function to erase a block.
drv_mark_bad_fn	Function to mark a bad block
drv_check_bad_fn	Function to check if a block is bad.
drv_initialise_fn	Function to initialise a device.
drv_deinitialise_fn	Function to deinitialise a device.

# Tracing mechanism
Yaffs has a lot of built in tracing to help debug and integrate. The tracing is controlled by yaffs_traceMask bitmask which allows various sets of tracing to be disabled or enabled at runtime.
The trace bits are specified in the yaffs_trace.h file.
The tracing mechanism has also been 'hijacked' to provide a control mask for extra verification code when the YAFFS_TRACE_VERIFYxxx trace bits are selected.
The tracing mechanism is readily integrated into the system via printf-like statements. Tracing is all done through macros which allow the strings to be converted into unicode or similar if need be.

# Linux
## Linux compile-time flags
The Linux compile time flags are documented in the Kconfig file and will not be duplicated here.
## Linux: /proc/yaffs trace adjustment
Under Linux, the tracing mechanism is hooked up to both the /proc/yaffs and the sys interface. The /proc/yaffs interface is very user friendly.
#cat +os > /proc/yaffs # Enables YAFFS_TRACE_OS
#cat -all+gc > /proc/yaffs # Disables everything then enable YAFFS_TRACE_GC
#cat 0xf000 > /proc/yaffs # Set trace mask to specified bitmask.
## Linux: /sys/ interface
The Linux /sys/ interface is used by many Linux OS components to access the state of control variables. Some Yaffs variables are available via /sys/module/yaffs2/parameters/ *. Values can be read and modified using standard shell commands or from application programs.
# ls /sys/module/yaffs2/parameters/ yaffs_auto_checkpoint yaffs_traceMask yaffs_wr_attempts
# cat /sys/module/yaffs2/parameters/yaffs_auto_checkpoint 1
# echo "2" > /sys/module/yaffs2/parameters/yaffs_auto_checkpoint
# cat /sys/module/yaffs2/parameters/yaffs_auto_checkpoint 2
Yaffs currently supports the following variables:
yaffs_auto_checkpoint: Controls when checkpoints should be written.
yaffs_traceMask: An alternative, and less user friendly,interface to modify tracing.
yaffs_wr_attempts: The number of attempts that Yaffs will make to write a chunk.
yaffs_gc_control: Controls the garbage collector.
## Linux: /proc/yaffs state dumping
Some of the state of Yaffs mounts can be determined by reading the /proc/yaffs entry.
# cat /proc/yaffs
charles@charles-laptop:/opt/y/cvs/yaffs2$ cat /proc/yaffs
YAFFS built:Mar 16 2010 11:52:25
$Id: yaffs_fs.c,v 1.101 2010-03-15 22:27:15 charles Exp $
$Id: yaffs_guts.c,v 1.119 2010-03-12 02:48:34 charles Exp $
Device 0 "NAND simulator partition 0"
startBlock......... 0
endBlock........... 511
totalBytesPerChunk. 2048
useNANDECC......... 1
noTagsECC.......... 0
isYaffs2........... 1
inbandTags......... 0
emptyLostAndFound.. 1
disableLazyLoad.... 0
refreshPeriod...... 10000
nShortOpCaches..... 10
nReservedBlocks.... 5
nDataBytesPerChunk. 2048
chunkGroupBits..... 0
chunkGroupSize..... 1
nErasedBlocks...... 152
blocksInCheckpoint. 0
nTnodesCreated..... 2300
nFreeTnodes........ 1852
nObjectsCreated.... 2300
nFreeObjects....... 1842
nFreeChunks........ 27843
nPageWrites........ 65993
nPageReads......... 19631
nBlockErasures..... 1133
nGCCopies.......... 37
garbageCollections. 161
passiveGCs......... 137
nRetriedWrites..... 0
nRetireBlocks...... 0
eccFixed........... 0
eccUnfixed......... 0
tagsEccFixed....... 0
tagsEccUnfixed..... 0
cacheHits.......... 44110
nDeletedFiles...... 0
nUnlinkedFiles..... 42917
refreshCount....... 1
nBackgroudDeletions 0

# Conclusions
Yaffs includes many options for changing speed or memory use, with specific flags for the Yaffs Direct Interface as well as Linux. Under Linux many of the control variables can be altered using standard Linux systems.